## Slide 1: Chapter 3: VLANs
Switched Networks
Notes: Cisco Networking Academy program
Switched Networks
Chapter 3: VLANs

## Slide 2: Chapter 3
3.1 VLAN Segmentation
3.2 VLAN Implementation
3.3 VLAN Security and Design
3.4 Summary
Notes: Chapter 3

## Slide 3: Chapter 3: Objectives
Explain the purpose of VLANs in a switched network.
Analyze how a switch forwards frames based on VLAN configuration in a multi-switched environment.
Configure a switch port to be assigned to a VLAN based on requirements.
Configure a trunk port on a LAN switch.
Configure Dynamic Trunk Protocol (DTP).
Troubleshoot VLAN and trunk configurations in a switched network.
Configure security features to mitigate attacks in a VLAN-segmented environment.
Explain security best practices for a VLAN-segmented environment.
Notes: Chapter 3 Objectives

## Slide 4: 3.1 VLAN Segmentation
Notes: Cisco Networking Academy program
Switched Networks
Chapter 3: VLANs

## Slide 5: Overview of VLANs VLAN Definitions
A VLAN is a logical partition of a Layer 2 network.
Multiple partitions can be created, allowing for multiple VLANs to co-exist.
Each VLAN is a broadcast domain, usually with its own IP network.
VLANs are mutually isolated and packets can only pass between them via a router.
The partitioning of the Layer 2 network takes place inside a Layer 2 device, usually via a switch.
The hosts grouped within a VLAN are unaware of the VLAN’s existence.
Notes: 3.1.1.1 VLAN Definitions

## Slide 6: Overview of VLANs VLAN Definitions (cont.)
Notes: 3.1.1.1 VLAN Definitions

## Slide 7: Overview of VLANs Benefits of VLANs
Security
Cost reduction
Better performance
Shrink broadcast domains
Improved IT staff efficiency
Simpler project and application management
Notes: 3.1.1.2 Benefits of VLANs

## Slide 8: Overview of VLANs Types of VLANs
Default VLAN
This is basically where ALL ports belongs to by default, this is technically VLAN 1 and it can't be deleted from the switch. On some (old) Catalyst switches you can't even disallow VLAN 1 from trunk ports.
Notes: 3.1.1.3 Types of VLANs

## Slide 9: Overview of VLANs Types of VLANs
Data VLAN
This is the "normal" VLAN where the traffic is carried and where the client data goes through the LAN.
Notes: 3.1.1.3 Types of VLANs

## Slide 10: Overview of VLANs Types of VLANs
Native VLAN:
The native VLAN is an 802.1Q only concept. Traffic belonging to the native VLAN is not tagged. Note that by default VLAN 1 (which is the default VLAN) is the native VLAN on ALL Catalyst switches. You can designate any VLAN as your native on your switch and note that it need to match on both ends of the trunk connection.
Notes: 3.1.1.3 Types of VLANs

## Slide 11: Overview of VLANs Types of VLANs
Voice VLAN:
The voice VLAN is where the QoS policies are applied in order to prioritize this traffic to send it through the LAN. The voice traffic it's always distinguished from the data traffic on the LAN.
Notes: 3.1.1.3 Types of VLANs

## Slide 12: Overview of VLANs Types of VLANs
Management VLAN:
This is used on a LAN for management purposes. Example of this would be to use it on a Out-of-Band (OOB) implementations. This VLAN normally carries sensitive traffic from a control perspective; some of the protocols that are carried on this VLAN are: FTP, TFTP, Telnet, SSH, SCP, and others.
Notes: 3.1.1.3 Types of VLANs

## Slide 13: Overview of VLANs Types of VLANs
Special VLANs:
These VLANs are basically used for special cases on your LAN. An example of a special case VLAN would be VLAN 0, which is used in conjunction with 802.1p. I would say that VLAN 1 fits in this "special" category too.
Notes: 3.1.1.3 Types of VLANs

## Slide 14: Overview of VLANs Types of VLANs
Reserved VLANs
There are some VLANs that are reserved internally on your switch in order to use them on other environments like FDDI, Token Ring. The specific VLANs used for these two types of networks are from 1002 - 1005.
Notes: 3.1.1.3 Types of VLANs

## Slide 15: Overview of VLANs Types of VLANs (cont.)
Notes: 3.1.1.3 Types of VLANs

## Slide 16: Overview of VLANs Voice VLANs
VoIP traffic is time-sensitive and requires:
  Assured bandwidth to ensure voice quality.
  Transmission priority over other types of network traffic.
  Ability to be routed around congested areas on the network.
  Delay of less than 150 ms across the network.
The voice VLAN feature enables access ports to carry IP voice traffic from an IP phone.
The switch can connect to a Cisco 7960 IP phone and carry IP voice traffic.
The sound quality of an IP phone call can deteriorate if the data is unevenly sent; the switch supports quality of service (QoS).
Notes: 3.1.1.4 Voice VLANs

## Slide 17: Overview of VLANs Voice VLANs (cont.)
The Cisco 7960 IP phone has two RJ-45 ports that each support connections to external devices.
  Network Port (10/100 SW) - Use this port to connect the phone to the network. The phone can also obtain inline power from the Cisco Catalyst switch over this connection.
  Access Port (10/100 PC) - Use this port to connect a network device, such as a computer, to the phone.
Notes: 3.1.1.4 Voice VLANs

## Slide 18: Overview of VLANs Voice VLANs (cont.)
Notes: 3.1.1.4 Voice VLANs

## Slide 19: VLANs in a Multi-Switched Environment VLAN Trunks
A VLAN trunk carries more than one VLAN.
A VLAN trunk is usually established between switches so same-VLAN devices can communicate, even if physically connected to different switches.
A VLAN trunk is not associated to any VLANs; neither is the trunk ports used to establish the trunk link.
Cisco IOS supports IEEE802.1q, a popular VLAN trunk protocol.
Notes: 3.1.2.1 VLAN Trunks

## Slide 20: VLANs in a Multi-Switched Environment VLAN Trunks (cont.)
Notes: 3.1.2.1 VLAN Trunks

## Slide 21: VLANs in a Multi-Switched Environment Controlling Broadcast Domains with VLANs
VLANs can be used to limit the reach of broadcast frames.
A VLAN is a broadcast domain of its own.
A broadcast frame sent by a device in a specific VLAN is forwarded within that VLAN only.
VLANs help control the reach of broadcast frames and their impact in the network.
Unicast and multicast frames are forwarded within the originating VLAN.
Notes: 3.1.2.2 Controlling Broadcast Domains with VLANs

## Slide 22: VLANs in a Multi-Switched Environment Tagging Ethernet Frames for VLAN Identification
Frame tagging is the process of adding a VLAN identification header to the frame.
It is used to properly transmit multiple VLAN frames through a trunk link.
Switches tag frames to identify the VLAN to that they belong. Different tagging protocols exist; IEEE 802.1Q is a vey popular example.
The protocol defines the structure of the tagging header added to the frame.
Switches add VLAN tags to the frames before placing them into trunk links and remove the tags before forwarding frames through nontrunk ports.
When properly tagged, the frames can transverse any number of switches via trunk links and still be forwarded within the correct VLAN at the destination.
Notes: 3.1.2.3 Tagging Ethernet Frames for VLAN Identification

## Slide 23: VLANs in a Multi-Switched Environment Tagging Ethernet Frames for VLAN Identification
Notes: 3.1.2.3 Tagging Ethernet Frames for VLAN Identification

## Slide 24: VLANs in a Multi-Switched Environment Native VLANs and 802.1Q Tagging
Frames that belong to the native VLAN are not tagged.
Frames received untagged remain untagged and are placed in the native VLAN when forwarded.
If there are no ports associated to the native VLAN and no other trunk links, an untagged frame is dropped.
In Cisco switches, the native VLAN is VLAN 1, by default.
Notes: 3.1.2.4 Native VLANs and 802.1Q Tagging

## Slide 25: VLANs in a Multi-Switched Environment Voice VLAN Tagging
Notes: 3.1.2.5 Voice VLAN Tagging

## Slide 26: 3.2 VLAN Implementations
Notes: Cisco Networking Academy program
Switched Networks
Chapter 3: VLANs

## Slide 27: VLAN Assignment VLAN Ranges on Catalyst Switches
Cisco Catalyst 2960 and 3560 Series switches support over 4,000 VLANs.
VLANs are split into two categories:
  Normal range VLANs
    VLAN numbers from 1 to 1,005
    Configurations stored in the vlan.dat (in the flash memory)
    VTP can only learn and store normal range VLANs
  Extended Range VLANs
    VLAN numbers from 1,006 to 4,096
    Configurations stored in the running configuration (NVRAM)
    VTP does not learn extended range VLANs
Notes: 3.2.1.1 VLAN Ranges On Catalyst Switches

## Slide 28: VLAN Assignment Creating a VLAN
Notes: 3.2.1.2 Creating a VLAN

## Slide 29: VLAN Assignment Assigning Ports to VLANs
Notes: 3.2.1.3 Assigning Ports To VLANs

## Slide 30: VLAN Assignment Assigning Ports to VLANs (cont.)
Notes: 3.2.1.3 Assigning Ports To VLANs

## Slide 31: VLAN Assignment Changing VLAN Port Membership
Notes: 3.2.1.4 Changing VLAN Port Membership

## Slide 32: VLAN Assignment Changing VLAN Port Membership (cont.)
Notes: 3.2.1.4 Changing VLAN Port Membership

## Slide 33: VLAN Assignment Deleting VLANs
Notes: 3.2.1.5 Deleting VLANs

## Slide 34: VLAN Assignment Verifying VLAN Information
Notes: 3.2.1.6 Verifying VLAN Information

## Slide 35: VLAN Assignment Verifying VLAN Information (cont.)
Notes: 3.2.1.6 Verifying VLAN Information

## Slide 36: VLAN Assignment Configuring IEEE 802.1q Trunk Links
Notes: 3.2.2.1 Configuring IEEE 802.1q Trunk Links

## Slide 37: VLAN Assignment Resetting the Trunk To Default State
Notes: 3.2.2.2 Resetting the Trunk To Default State

## Slide 38: VLAN Assignment Resetting the Trunk To Default State (cont.)
Notes: 3.2.2.2 Resetting the Trunk To Default State

## Slide 39: VLAN Assignment Verifying Trunk Configuration
Notes: 3.2.2.3 Verifying Trunk Configuration

## Slide 40: Dynamic Trunking Protocol Introduction to DTP
Switch ports can be manually configured to form trunks.
Switch ports can also be configured to negotiate and establish a trunk link with a connected peer.
The Dynamic Trunking Protocol (DTP) manages trunk negotiation.
DTP is a Cisco proprietary protocol and is enabled, by default, in Cisco Catalyst 2960 and 3560 switches.
If the port on the neighbor switch is configured in a trunk mode that supports DTP, it manages the negotiation.
The default DTP configuration for Cisco Catalyst 2960 and 3560 switches is dynamic auto.
Notes: 3.2.3.1 Introduction to DTP

## Slide 41: Dynamic Trunking Protocol Negotiated Interface Modes
Cisco Catalyst 2960 and 3560 support the following trunk modes:
  Switchport mode dynamic auto
  Switchport mode dynamic desirable
  Switchport mode trunk
  Switchport nonegotiate
Notes: 3.2.3.2 Introduction to DTP

## Slide 42: Troubleshooting VLANs and Trunks IP Addressing Issues with VLAN
It is a common practice to associate a VLAN with an IP network.
Because different IP networks only communicate through a router, all devices within a VLAN must be part of the same IP network to communicate.
The figure displays that PC1 cannot communicate to the server because it has a wrong IP address configured.
Notes: 3.2.4.1 IP Addressing Issues with VLAN

## Slide 43: Troubleshooting VLANs and Trunks Missing VLANs
If all the IP addresses mismatches have been solved, but the device still cannot connect, check if the VLAN exists in the switch.
Notes: 3.2.4.2 Missing VLANs

## Slide 44: Troubleshooting VLANs and Trunks Introduction to Troubleshooting Trunks
Notes: 3.2.4.3 Introduction to Troubleshooting Trunks

## Slide 45: Troubleshooting VLANs and Trunks Common Problems with Trunks
Trunking issues are usually associated with incorrect configurations.
The most common type of trunk configuration errors are:
  Native VLAN mismatches
  Trunk mode mismatches
  Allowed VLANs on trunks
If a trunk problem is detected, the best practice guidelines recommend to troubleshoot in the order shown above.
Notes: 3.2.4.4 Common Problems With Trunks

## Slide 46: Troubleshooting VLANs and Trunks Trunk Mode Mismatches
If a port on a trunk link is configured with a trunk mode that is incompatible with the neighboring trunk port, a trunk link fails to form between the two switches.
Use the show interfaces trunk command to check the status of the trunk ports on the switches.
To fix the problem, configure the interfaces with proper trunk modes.
Notes: 3.2.4.5 Trunk Mode Mismatches

## Slide 47: Troubleshooting VLANs and Trunks Incorrect VLAN List
VLANs must be allowed in the trunk before their frames can be transmitted across the link.
Use the switchport trunk allowed vlan command to specify which VLANs are allowed in a trunk link.
Use the show interfaces trunk command to ensure the correct VLANs are permitted in a trunk.
Notes: 3.2.4.6 Incorrect VLAN List

## Slide 48: 3.3 VLAN Security and Design
Notes: Cisco Networking Academy program
Switched Networks
Chapter 3: VLANs

## Slide 49: Attacks on VLANs Switch Spoofing Attack
There are a number of different types of VLAN attacks in modern switched networks; VLAN hopping is one example.
The default configuration of the switch port is dynamic auto.
By configuring a host to act as a switch and form a trunk, an attacker could gain access to any VLAN in the network.
Because the attacker is now able to access other VLANs, this is called a VLAN hopping attack.
To prevent a basic switch spoofing attack, turn off trunking on all ports, except the ones that specifically require trunking.
Notes: 3.3.1.1 Switch Spoofing Attack

## Slide 50: Attacks on VLANs Double-Tagging Attack
Double-tagging attack takes advantage of the way that hardware on most switches de-encapsulate 802.1Q tags.
Most switches perform only one level of 802.1Q de-encapsulation, allowing an attacker to embed a second, unauthorized attack header in the frame.
After removing the first and legit 802.1Q header, the switch forwards the frame to the VLAN specified in the unauthorized 802.1Q header.
The best approach to mitigating double-tagging attacks is to ensure that the native VLAN of the trunk ports is different from the VLAN of any user ports.
Notes: 3.3.1.2 Double-Tagging Attack

## Slide 51: Attacks on VLANs Double-Tagging Attack (cont.)
Notes: 3.3.1.2 Double-Tagging Attack

## Slide 52: Attacks on VLANs PVLAN Edge
The Private VLAN (PVLAN) Edge feature, also known as protected ports, ensures that there is no exchange of unicast, broadcast, or multicast traffic between protected ports on the switch.
Local relevancy only.
A protected port only exchanges traffic with unprotected ports.
A protected port does not exchange traffic with another protected port.
Notes: 3.3.1.3 PVLAN Edge

## Slide 53: Design Best Practices for VLANs VLAN Design Guidelines
Move all ports from VLAN 1 and assign them to a not-in-use VLAN
Shut down all unused switch ports.
Separate management and user data traffic.
Change the management VLAN to a VLAN other than VLAN 1. (The same goes to the native VLAN.)
Ensure that only devices in the management VLAN can connect to the switches.
The switch should only accept SSH connections.
Disable autonegotiation on trunk ports.
Do not use the auto or desirable switch port modes.
Notes: 3.3.2.1 VLAN Design Guidelines

## Slide 54: Chapter 3: Summary
This chapter:
Introduced VLANs and their types
Described the connection between VLANs and broadcast domains
Discussed IEEE 802.1Q frame tagging and how it enables differentiation between Ethernet frames associated with distinct VLANs as they traverse common trunk links.
Examined the configuration, verification, and troubleshooting of VLANs and trunks using the Cisco IOS CLI and explored basic security and design considerations.
Notes: Chapter 3 Summary